| Date | Révision | Evolutions du document | Auteur |
| --- | --- | --- | --- |
| 18/01/16 | 0 | Creation | JS |
| 25/20/2016 | 1 |  | JS |
| Numéro de série du flotteur Float Serial Number : | AI2600-16 IT 004_005 |
| MISSION COMMANDS |
| Abbr. | NAME | DEFAULT VALUE | UNIT | REQUEST VALUE |
| MC0 | MC0 – Number of cycles | 300 | - | 500 |
| MC1 | MC1 – Number of cycles with « Cycle Period 1 » | 300 | - | 500 |
| MC2 | MC2 – Cycle Period 1 | 240 | Hours | 240 |
| MC3 | MC3 – Cycle Period 2 | 240 | Hours | 240 |
| MC4 | MC4 – Reference Day (1) | 2 | Mission day | 2 |
| MC5 | MC5 - Estimated hour on surface (1) | 6 | Hour in the day | 6 |
| MC6 | MC6 – Delay Before Mission | 0 | Minutes | 0 |
| MC7 | MC7 – CTD acquisition mode | 1 | - | 1 |
| MC8 | MC8 – Descent Sampling Period | 0 | Seconds | 0 |
| MC9 | MC9 – Drift Sampling Period | 12 | Hours | 12 |
| MC10 | MC10 – Ascent Sampling Period | 10 | Seconds | 10 |
| MC11 | MC11 – Drift Depth during MC1 cycles | 1000 | dBar | 1000 |
| MC12 | MC12 – Profile Depth during MC1 cycles | 2000 | dBar | 2000 |
| MC13 | MC13 – Drift Depth after MC1 cycles, up to MC0 cycles | 1000 | dBar | 1000 |
| MC14 | MC14 – Profile Depth after MC1 cycles, up to MC0 cycles | 2000 | dBar | 2000 |
| MC15 | MC15 – Alternate profile period | 1 | - | 1 |
| MC16 | MC16 - Alternate Profile pressure | 2000 | dBar | 2000 |
| MC17 | MC17 - Threshold Middle/Surface Pressure | 10 | dBar | 100 |
| MC18 | MC18 - Threshold Middle/Bottom Pressure | 200 | dBar | 700 |
| MC19 | MC19 - Thickness of the surface layers | 1 | dBar | 2 |
| MC20 | MC20 - Thickness of the middle layers | 10 | dBar | 10 |
| MC21 | MC21 - Thickness of the bottom layers | 25 | dBar | 25 |
| MC22 | MC22 - End of life Iridium period (Iridium Only) | 60 | Minutes | 60 |
| MC23 | MC23 – Iridium 2nd session wait period (Iridium only) | 0 | Minutes | 0 |
| MC24 | MC24 - Grounding mode (0 = Shift, 1 = Stay grounded) | 0 | Minutes | 0 |
| MC25 | MC25 – Grounding switch pressure (Minus Pressure profile) | 100 | dBar | 100 |
| MC26 | MC26 – Wait at surface in case of grounding at surface | 10 | Minutes | 10 |
| MC27 | MC27 – Optode Type (0 = none, 1 = 4330, 2 = 3830) | 0 | - | 0 |
| MC28 | MC28 – CTD Sensor Cut-Off pressure | 5 | dBar | 5 |
| MC29 | MC29 – In air Acquisition Period | 0 | - | 0 |
| MC30 | MC30 – In air acquisition sampling period | 30 | Seconds | 30 |
| MC31 | MC31 – In Air acquisition duration | 5 | Minutes | 5 |

Armed mode ON		:	( Yes			( No

Shipping Adress

Nke comments 			:

Options Required:

# Dongle of PC Bluetooth communication (  ):					# of Deployment Boxes:

Other Request: